Binning procedure for xray flare ionization parameterization.
Break up the three shortest wavelength bins of Solomon and Qian into 12 higher resolution bins. Bins to be expanded are the 0.5-4 A, 4-8A and 8-18A

Bin #	 min λ	 max λ	Mean λ (A)	Mean σN2abs / (mega-barns)	Alt of tau=1 (km)
1	0.5	1	0.75	2.48e-5	43
2	1	1.5	1.25	1.47e-4	55.5
3	1.5	2	1.75	4.57e-4	63.5
4	2	2.5	2.25	1.02e-3	69.1
5	2.5	3	2.75	1.9e-3	73.3
6	3	4	3.5	4.0e-3	78.7
7	4	5	4.5	8.55e-3	84
8	5	6	5.5	1.55e-2	88.1
9	6	8	7	3.12e-2	93
10	8	10	9	6.32e-2	98
11	10	14	12	0.14	103.5
12	14	18	16	0.30	109

The n2 cross section comes from Henke where I doubled the atomic nitrogen values they give to get N2. A test of this at 23.5 angstroms gave 7.95E-19 cm -2 and at 24 angstrom, 8.3E-19 cm-2 and Judy Fennelly’s table has 8E-19 at 23.7 angstroms. The altitudes are derived from assuming an exponential density with constant scale height (= 7 km) and solving tau = 1 = n(z)*sigma*H, for z. Overhead sun is assumed. If there is a 60 degree zenith angle, the altitudes of tau =1 go up by 5 km or so. The selection of bins gives roughly 5 km resolution between 60-100 km.