Verification of calculated and model values of altitude of optical depth

---
Theoritical Calculation of altitude of unit optical depth- Table data
Calculated	Results
Bin #	λ min (A)	λ max (A)	Mean λ (A)	Mean σN2abs / (mega-barns)	Alt of tau=1 (km)
1	0.5	1	0.75	2.48e-5	43
2	1	1.5	1.25	1.47e-4	55.5
3	1.5	2	1.75	4.57e-4	63.5
4	2	2.5	2.25	1.02e-3	69.1
5	2.5	3	2.75	1.9e-3	73.3
6	3	4	3.5	4.0e-3	78.7
7	4	5	4.5	8.55e-3	84
8	5	6	5.5	1.55e-2	88.1
9	6	8	7	3.12e-2	93
10	8	10	9	6.32e-2	98
11	10	14	12	0.14	103.5
12	14	18	16	0.30	109
"" %tau (z) =1 =%sigma^a H n(z) newline "" Exponential density: n(z)=n_0 exp left( {-z} over {H} right ) newline "" Altitude of unit optical depth: z = H ln left( H n_0 %sigma^a right) newline "" Assuming: Scale Height H= 7km, n_0= 2.7e19 cm^-3, %sigma^a for N_2 as given, newline "" we find the value for z for optical depth %tau =1 by using the above formula
6/21/20

---
        Effect of altitude bin ∆z
If we take the altitude bin in the model to be ∆z= 0.5 to 1 km, the deviation in calculating the altitude of unit optical depth is minimum, so ∆z= 1 km in the model.
Calculated	Results
Bin #	λ min (A)	λ max (A)	Mean λ (A)	Mean σN2abs / (mega-barns)	Alt of tau=1 (km)
1	0.5	1	0.75	2.48e-5	43
2	1	1.5	1.25	1.47e-4	55.5
3	1.5	2	1.75	4.57e-4	63.5
4	2	2.5	2.25	1.02e-3	69.1
5	2.5	3	2.75	1.9e-3	73.3
6	3	4	3.5	4.0e-3	78.7
7	4	5	4.5	8.55e-3	84
8	5	6	5.5	1.55e-2	88.1
9	6	8	7	3.12e-2	93
10	8	10	9	6.32e-2	98
11	10	14	12	0.14	103.5
12	14	18	16	0.30	109
Altitued Difference (km)
3
2.5
1.5
1.9
1.7
0.3
1
1.1
3
4
4.5
6
Model Results
σN2abs / (mega-barns)	Alt of tau=1 (km)	Exact value of optical depth tau
3.38E-05	46	1.12
1.49E-04	58	1.02
4.55E-04	65	1.32
1.03E-03	71	1.21
2.04E-03	75	1.26
3.91E-03	79	1.25
8.59E-03	83	1.39
1.56E-02	87	1.22
3.15E-02	90	1.17
6.43E-02	94	1.15
1.41E-01	99	1.24
3.02E-01	103	1.31

---
N2 Cross-sections
I changed the cross-sections of N2 in the model to the one from the table.
The cross-section of the first bin is different in the model and the table.
Changing the cross-sections only changes the altitude of unit optical depth in the first bin.
I checked the Henke + Fennelly data, and the model value is more accurate than the table value.

---
N2 Cross-sections
Calculated	Results
Bin #	λ min (A)	λ max (A)	Mean λ (A)	Mean σN2abs / (mega-barns)	Alt of tau=1 (km)
1	0.5	1	0.75	2.48e-5	43
2	1	1.5	1.25	1.47e-4	55.5
3	1.5	2	1.75	4.57e-4	63.5
4	2	2.5	2.25	1.02e-3	69.1
5	2.5	3	2.75	1.9e-3	73.3
6	3	4	3.5	4.0e-3	78.7
7	4	5	4.5	8.55e-3	84
8	5	6	5.5	1.55e-2	88.1
9	6	8	7	3.12e-2	93
10	8	10	9	6.32e-2	98
11	10	14	12	0.14	103.5
12	14	18	16	0.30	109
Alt of tau=1 (km)	Exact value of optical depth tau
45	1.12
58	1.02
65	1.32
71	1.21
75	1.26
79	1.25
83	1.39
87	1.22
90	1.17
94	1.15
99	1.24
103	1.31
Altitued Difference (km)
2
2.5
1.5
1.9
1.7
0.3
1
1.1
3
4
4.5
6
This bin changed

---
    Estimation of n0 from the model
n0 (cm3)	Height of unit optical depth (km)	Scale Height (km)
1.63e+19	45	7.82
3.01e+19	58	7.19
5.72e+19	65.5	6.70
1.13e+20	71	6.34
1.86e+20	75	5.95
2.45e+20	79	5.60
6.31e+20	83.5	5.27
1.84e+21	87	5.27
1.58e+21	90.5	5.30
9.81e+20	94.5	5.45
1.19e+21	99	5.40
5.36e+20	103	5.62
In the table (slide 2), it was assumed n0= 2.7E19 cm3
I used the formula from slide 2, to get an estimation of n0 of the model.
This combination of scale height and density gives the same value of altitude of unit optical depth as in slide 5

---
Estimation of altitude of unit optical	depth using constant n0
n0 (cm3)	Height of unit optical depth (km)	Scale Height (km)
2.7e+19	48.9	7.82
2.7e+19	57	7.19
2.7e+19	60.5	6.70
2.7e+19	62	6.34
2.7e+19	63	5.95
2.7e+19	65.9	5.60
2.7e+19	65.9	5.27
2.7e+19	64.8	5.30
2.7e+19	68.9	5.30
2.7e+19	74.9	5.45
2.7e+19	78.5	5.40
2.7e+19	86.2	5.62
However, if I use n0= 2.7E19 cm3 , the model’s scale height, and the formula for altitude of unit optical height derived in slide 2, the altitude is very different (column2 of table on the right)
So the correct scale height and density is required to get the correct altitude.

---
Calculation of altitudes with MSIS values of n0
Calculated	Results
Bin #	λ min (A)	λ max (A)	Mean λ (A)	Mean σN2abs / (mega-barns)	Alt of tau=1 (km) n0= 2.7 E19
1	0.5	1	0.75	2.48e-5	43
2	1	1.5	1.25	1.47e-4	55.5
3	1.5	2	1.75	4.57e-4	63.5
4	2	2.5	2.25	1.02e-3	69.1
5	2.5	3	2.75	1.9e-3	73.3
6	3	4	3.5	4.0e-3	78.7
7	4	5	4.5	8.55e-3	84
8	5	6	5.5	1.55e-2	88.1
9	6	8	7	3.12e-2	93
10	8	10	9	6.32e-2	98
11	10	14	12	0.14	103.5
12	14	18	16	0.30	109
The MSIS value for n0= 1.9 E19 cm3
Taking scale height H= 7km and the formula for altitude of unit optical height derived in slide 2, and calculating the altitude of unit optical depth.
The altitudes are different than the ones calculated in the table with n0= 2.7E19 cm3
Alt of tau=1 (km) (n0= 1.9 E19)
40.6
53.
61
66.6
71
76
81.5
85.6
90.6
95.5
101
106
Model Results
Alt of tau=1 (km)
46
58
65
71
75
79
83
87
90
94
99
103

---
Conclusion
The difference in altitude of unit optical depth between the model data and the calculated data is due to the difference in the assumptions made in its calculations and the different values calculated by the model.
An altitude binning of ∆z= 0.5 to 1 km is good for getting the correct altitude of optical depth.
The N2 cross-section of the first bin in the model is more accurate than that given in the theoretical table.